## Slide 1: Computing Scattering Intensities with Sassena
Jose M. Borreguero
Neutron Data Analysis and Visualization Division
Center for Accelerating Materials Modelling
SHUG-15

## Slide 2: What is ?
http://www.sassena.org/
“Sassena is a highly scalable parallelized software for calculating neutron and X-ray scattering intensities from molecular dynamics simulations.”

## Slide 3: Contents
What does Sassena compute?
Features
Reference

## Slide 4: Coherent Scattering
Coherent intermediate (time-dependent) dynamic structure factor
system amplitude, for
every trajectory frame
crystal (phonons)
cell membrane
anisotropic system
solvent
micro-crystalline powder
isotropic system

## Slide 5: Incoherent scattering
Incoherent intermediate (time-dependent) dynamic structure factor
intensity for each atom
solvent
crystalline powder
isotropic system
anisotropic diffusion under external field

## Slide 6: Long Time Value
Configurations at and are not correlated when
No correlations means much faster to compute
Fast experiment (<1hour)
Diffraction

## Slide 7: Summary
coherent
incoherent
correlation intensity amplitude
real real complex
Example: time evolution of the static structure factor under isotropic expansion

## Slide 8: Advantages and Disadvantages
Linearly scale up to 7000 cores
Handles millions of atoms
Not for windows computers
   However cygwin, or virtual machine
Not easy to install
Input configuration file, no GUI ?

## Slide 9: Input Options
Some features:
Database of atomic structure factors
Atom selection
Configuration selection
vector selection
Averages in space
Reference: Github  Sassena  reference_input_configurations.pdf
All input options are specified in a single file
Walkthrough: Github  sassena  input_example.xml

## Slide 10: Input Options
All input options are specified in a single file
Walkthrough: Github  sassena  input_example.xml
 Options for the input data
 Options for the type of scattering
 Algorithm to carry out the number crunching
 Atomic structure factors

## Slide 11: Sample Section
 List of atom names
 atomic trajectory
 atom selection

## Slide 12: Stager Section
 relevant subsystem

## Slide 13: Scattering Section
 Incoherent (all for coherent)
 fqt

## Slide 14: Scattering.Vectors
{ (0.1, 0, 0),
(0.2, 0, 0),
..
(6.3, 0, 0) }
 List of vectors for which to compute

## Slide 15: Scattering.average
{ (0.1, 0, 0),
…
(, 0, 0),
..
(6.3, 0, 0) }



…

## Slide 16: Scattering.signal
 Single output file





## Slide 17: Reference and Guide
Reference:
B. Lindner and J. C. Smith, Computer Physics Communications 183 (7) 1491-1501
Github  sassena reference_paper.pdf
Guide:
Github  sassena  reference_input_configurations.pdf